Open University System Programming Lab Course Assembler Project Specification
Document written by Vladislav Panin

Project made by Vladislav Panin and Itay Krishtal

The goal of the project is to create an assembler for the assembly language, the properties and specification of which will be discussed later in the document.

The linkage and loading stages are outside of the scope of this project.

MACHINE DATA

The imaginary machine, that will run the programs written on the provided assembly language, has the following characteristics:
1) Processor – has the PSW register.
2) Registers.
3) RAM, a part of which is the stack.

Registers:
*) There are 8 registers: r0, r1, r2, r3, …, r7.
*) Every register can hold 15 bits of data.
*) Names of the registers always are in the format r#, where # is the number between 0 and 7.
*) Least significant bit is 0, most significant bit is 14.

Processor:
*) The processor contains a register, named PSW (Program Status Word). It has a number of flags to determine the state of the processor.

RAM:
*) RAM size is 4096 words (labeled 0-4095 in the 10 base). Every word has the size of 15 bits. The format of each word is similar to the format of the registers.

General Machine Data:
*) The machine accepts only integers as operands – there is no support for other real numbers.
*) The arithmetic is done with the 2’s compliment method.
*) The machine supports characters, formatted in ASCII.

INSTRUCTION FORMAT
Every instruction is encoded into several consecutive memory words, starting from one word and up to three words – the amount of words depends on the source and target operand modes of the instruction (will be discussed later).

In the output file of the assembler, every word is encoded into octal base (base-8) number sequence.

In every type of instruction, the first word is always the same. It also determines the structure of the instruction.

First instruction word:

The following picture shows the format of the first instruction word:

Bits 11-14 contain the opcode of the instruction. The ISA of our machine supports 16 opcodes – each opcode is symbolically represented by an operation name.

Bits 3-6 contain the target (destination) operand mode. Every mode has it’s representative bit – it’s value is 1 if the target operand is to be treated via this mode, and 0 otherwise. If there is no target operand, every mode has 0 in it’s relevant bit position.

Bits 7-10 contain the source operand mode. Every mode has it’s representative bit – it’s value is 1 if the source operand is to be treated via this mode, and 0 otherwise. If there is no source operand, every mode has 0 in it’s relevant bit position.

Bits 0-2 (The “A,R,E” fields) contain the A,R,E flag data – Absolute, Relocatable, External. These flags mean the following:

“A” (Absolute) – the instruction is not dependent on it’s location in memory. This is valid for instructions with immediate operands, and, for example, not valid for labels.

“R” (Relocatable) – the instruction depends on it’s location in memory. This is valid, for example, for labels – changing their position in memory means changing the label’s position in the program structure.

“E” (External) – the instruction depends on an external symbol (for example, a label that is defined in another code file).

In each instruction, the A,R,E, flags will contain exactly one flag that is ‘on’ (contains the value 1) and others ‘off’ (value 0). The first instruction word will always have the A flag set to 1, and others as 0.

Operand modes:

The assembly of our machine has four operand modes, that are labeled 0, 1, 2, 3. The operand modes for the instruction are encoded in the machine language with the instruction. Each operand required an additional word.

If there are two operands in an instruction, first will appear the additional word for the target (destination) operand, and then the word for the source operand. There is also an exception case, in which both operands’ modes are encoded with one word.

Each such additional word is encoded in one of the three possible encoding methods, and the type of method is determined by the A, R, E, flags. The type of encoding can be known by checking which flag has the value 1.

“A” mode does not require linking and loading steps changes.
“R” mode requires changes in the linking and loading steps.
“E” mode requires changes in the linking and loading steps.

The following table shows and explains the possible operand modes:

Example	How the operand is written in the assembly code	Content of the additional operand encoding word	Operand Mode	Operand Mode Number
mov #-1,r2 / In this example the first operand of the command (the source operand) is given in the immediate mode. / The command writes the integer ‘-1’ into the r2 register.	The operand begins with the # symbol and immediately followed by base-10 integer.	The additional operand encoding word contains the operand itself, which is an integer represented in the 2’s-complement method by 12 bits, and is located in the bits 3-14 of the word. The 0-2 bits are the ARE flags, where A is 1 and others are 0.	Immediate Mode	0
The following line defines the label ‘x’: / x: .data 23 / The following line decreases the content of the word, stored at the address x in the memory, by 1: / dec x / So, in this example ‘x’ is like a variable of sorts.	The operand is a label that was defined previously, or will be defined in the future. The definition is made by prefixing a command “.string” or “.data” with the label name, or prefixing an instruction, or by using “.extern”. / Label is a symbolic representation of a memory address.	The additional operand encoding word contains an address in memory. The word, that is stored in that address, is the operand. The address is represented as an unsigned integer with the size of 12 bits, and is stored in the bits 3-14 of the instruction. / The ARE flags are stored in bits 0-2, and in this mode the flags are dependent on the address type in bits 3-14. / If it’s an address, which represents a line from the current program source file, then the R flag is enabled (value 1), and others are 0. / If it’s an address, which represents a line from a different source file, the E flag is enabled (value 1) and others are 0.	Direct Mode	1
inc *r1 / In this example the command inc increases the content of the word, to which points the address stored in r1, by 1. / Additional example: / mov *r1,*r2 / In this example the mov instruction copies the content of the word, that is located at the address, to which the address, stored in the registry r1, points, into the location, to which the address in the r2 points. / The content of the registers itself is not changed. / Both operands are written in the Indirect Register Mode in the last example, therefore they will be encoded with one (shared) additional operand encoding word.	The operand starts with * and is followed by a registry.	This operand mode is used to access memory by using a pointer, located in a registry. Content of the registry is treated as a memory address, and the operand is the word located at that address. The address is represented as an unsigned integer with the size of 15 bits. / If the operand is the target operand, the additional operand encoding word will contain at bits 3-5 the number of the register, that is used as a pointer. / If the operand is the source operand, the bits used are 6-8. / The ARE flags are at bits 0-2, and in this mode the A flag is 1 and others are 0. / If the instruction uses both operands with the Indirect Register Mode or Direct Register Mode, both registers will share the additional operand encoding word, where bits 5-3 will have the target operand number, and 6-8 will have the source operand number. / Unused bits of the additional operand encoding word will be set to 0.	Indirect Register Mode	2
clr r1 / In this example the clr instruction clears (sets to 0) the content of the registry 1. / Additional example: / mov r1,*r2 / In this example, the mov command will copy the content of the registry r1, into the word in memory, to which the address stored in r2 points. / r1 is provided in the Direct Register Mode, and *r2 provided in the Indirect Register Mode, therefore they will share the additional operand encoding word.	The operand is the register name.	The operand is the register – specifically, what is stored in it. / If the operand is the target operand, the additional operand encoding word will contain at bits 3-5 the number of the register, that is used as a pointer. / If the operand is the source operand, the bits used are 6-8. / The ARE flags are at bits 0-2, and in this mode the A flag is 1 and others are 0. / If the instruction uses both operands with the Indirect Register Mode or Direct Register Mode, both registers will share the additional operand encoding word, where bits 5-3 will have the target operand number, and 6-8 will have the source operand number. / Unused bits of the additional operand encoding word will be set to 0.	Direct Register Mode	3

MACHINE INSTRUCTION SET

The following picture shows the opcodes of the machine:

The operation name is always written in lowercase.

The instructions are divided into three groups – the groups are formed by amount of operands each instruction takes.

First group – requires two operands:
The following table provides the description and information on the available instructions of the machine in this group:
Example Explanation	Example	What is done	opcode (base-10)	Instruction
Copy the content of the variable A (word at the address in memory to which A points) into the registry r1.	mov A, r1	Performs a copy of the source operand into the target operand.	0	mov
If the content of the variable A is similar to the content of the registry r1, then the Z-flag in the PSW registry will be set to 1, otherwise to 0.	cmp A, r1	Performs a comparison between the two operands. / The comparison is done like this: The content of the target operand is subtracted from the content of the source operand without saving the subtraction result. / The subtraction updates the Z (“Zero-Flag”) flag in the PSW processor registry.	1	cmp
r0 is set to the result of the operation (content of A + content of r0)	add A, r0	Target operand (the second one) receives the result of the addition of the target operand and the source operand (the first one)	2	add
r1 is set to (r1 - 3)	sub #3, r1	Target operand receives the result of the subtraction of the source operand from the target operand	3	sub
The address, that HELLO represents, is written into the r1 registry.	lea HELLO, r1	lea is the acronym for Load Effective Address. The instruction copies the address, represented by the source operand into the target operand.	4	lea

Second group – requires one operand:
Encoding of the operand of the instructions of this group is done by encoding it into the target operand. Bits 7-10, which represent the source operand, have 00 written in them, since they have no meaning.

The following table provides the description and information on the available instructions of the machine in this group:
Example Explanation	Example	What is done	opcode (base-10)	Instruction
r2 ← 0	clr r2	Operand’s contents are set to 0.	5	clr
r2 ← not r2	not r2	Reverse the bit values in the operand. (0 to 1, 1 to 0)	6	not
r2 ← r2 + 1	inc r2	Increase the operand content by 1	7	inc
C ← C - 1	dec r2	Decrease the operand content by 1	8	dec
PC ← LINE / The Program Counter pointer receives the address, that is represented by LINE, and therefore the program execution will proceed from the command at that address.	jmp LINE	Jump the program execution to the address, that is in the operand. / It’s an execution flow control command. / Execution of this command updates the Program Counter with the operand content.	9	jmp
If the Z-flag in the PSW is 0, then: / PC ← LINE	bne LINE	bne is an acronym for Branch if Not Equal: / In this case, it’s Branch if Not Equal to zero. / It’s an execution flow control command. / If the Z-flag in PSW is zero, then the execution of the program will proceed from the address, represented by LINE.	10	bne
The ASCII code of the received input will be stored at r1.	red r1	Read a symbol from the standard input (stdin) into the operand.	11	red
The character, the ASCII code of which is at r1, will be printed to the stdout.	prn r1	Print the symbol, located at the operand, into the standard output (stdout).	12	prn
push(PC) / PC ← FUNC	jsr FUNC	Call the procedure (subroutine) FUNC. / The current PC address is pushed onto the stack. / It’s an execution flow control command.	13	jsr

Third group – requires no operands:

The operands are encoded with 0 in the respective bits.

The following table provides the description and information on the available instructions of the machine in this group:
Example Explanation	Example	What is done	opcode (base-10)	Instruction
PC ← pop()	rts	Returning from the subroutine. / The value, that is at the head of the stack, is popped and put into the PC.	14	rts
The program stops.	stop	Stops the execution of the program.	15	stop